## Slide 1
V2X
Autonomous Emergency Vehicle Priority Platform
Authenticated V2X emergency signalling — from cryptographic session establishment to physical lane evasion — on real autonomous robots, on real hardware, with no simulation.
Applied Cryptography
Computer Vision
Embedded Systems
Autonomous Robotics
V2X Networking
Siliris Technologies Pvt. Ltd. · 2026

## Slide 2
THE DEMO
What You See
1
An emergency vehicle approaches from behind
It cryptographically authenticates itself with a roadside unit.
2
Roadside unit issues a signed emergency event
Encrypted broadcast sent to all vehicles on the subnet.
3
Car cross-checks the ambulance's position
Direct Pi-to-Pi UDP — no laptop needed. Decides autonomously to yield.
4
Car moves to the inner edge
Ambulance passes. Car recovers and resumes speed.
TRACK LAYOUT
┌────────────────────────┐
│ outer yellow boundary │
│ ┌──────────────────┐ │
│ │ white oval lane │ │
│ │ ┌────────────┐ │ │
│ │ │yellow inner│ │ │
│ │ │island │ │ │
│ │ │(yield zone)│ │ │
│ │ └────────────┘ │ │
│ └──────────────────┘ │
└────────────────────────┘
→ Clockwise direction of travel
→ 10 ft × 12 ft arena
→ 10 AprilTag zones
No human presses a button at any stage · No simulation · 9.4 ms auth latency

## Slide 3
HARDWARE
The Wolf Platform
🤖 Chassis
• Powder-coated aluminium frame
• High-grip wheels
• Ring-lit camera mount
• Purpose-built — not a dev kit
⚡ Motor Controller
• Custom STM32F405 PCB (designed & fabricated)
• RTOS — guaranteed 20 Hz control loop
• Hardware encoders on all 4 wheels
• Lyra binary protocol over UART
📷 Sensing
• ArduCam 8MP IMX219
• Downward-facing at ~350 mm height
• Lane detection + AprilTag at 20 Hz
• 320×240 px processing resolution
🖥️ Compute
• Raspberry Pi 5 on each robot
• Full autonomy stack on-device
• No cloud, no ROS at runtime
• C++ OBU + Python vision in parallel
20 Hz
MOTOR CONTROL LOOP
4
HARDWARE ENCODERS
RTOS
GUARANTEED TIMING
Custom PCB
STM32F405 FABRICATED
Pi 5
ON-DEVICE COMPUTE

## Slide 4
ARCHITECTURE
Two Systems. One Integration.
LAPTOP / DESKTOP PC
↳ Desktop server (Flask + WebSocket) :5000
↳ Issues cryptographic keys to all entities
↳ Runs the live authentication dashboard
↳ RSU binary (C++) — UDP :5000
↳ Authenticates OBU packets
↳ Broadcasts EMERGENCY_ACTIVE → :5001
CAR Pi (v2x-car-01)
↳ Camera → lane follower → emergency handler → motors
↳ OBU subprocess (C++) — authenticates with RSU
↳ RSU alert listener UDP :5001
↳ Position broadcaster UDP :5002 ↔ ambulance
↳ Heartbeat → laptop every 15 s
↳ MJPEG vision stream :5005
AMBULANCE Pi (v2x-emgy)
↳ Camera → lane follower → drives straight through
↳ OBU re-authenticates every ~2 s
↳ Posts is_emergency: true → keeps ACTIVE alive
↳ Position broadcaster UDP :5002 ↔ car
↳ Heartbeat → laptop every 15 s
↳ MJPEG vision stream :5005
Startup order: ① Desktop server → ② RSU binary → ③ Car Pi → ④ Ambulance Pi

## Slide 5
V2X SECURITY
32-Step Mutual Authentication Protocol
1
Registration (one-time)
Desktop generates EC P-256 keypairs. Issues RID, AID, SK, PK_self, PK_RSU to each OBU.
2
AuthRequest — Ambulance OBU → RSU
PID | timestamp | ECDH_encapsulate(PK_RSU) | ECDSA_sign(SK)
3
RSU validates + derives session keys
Timestamp ±500ms check → ECDSA verify → ECDH decapsulate → HKDF → SK_enc + SK_mac
4
Mutual key confirmation KC1 / KC2
Both sides prove they derived the same session keys — mutual authentication.
5
Post-auth AES-256-GCM message
{"entity_id": "V2X_EMGY", "is_emergency": true} → RSU broadcasts EMERGENCY_ACTIVE
WHY EACH MECHANISM EXISTS
Timestamp ±500ms
Prevents replay attacks
ECDSA signature
Prevents packet forgery
ECDH encapsulation
Prevents man-in-the-middle
AES-256-GCM
Prevents eavesdropping
HMAC-SHA-256
Prevents ciphertext bit-flip
KC1/KC2 exchange
Ensures mutual key confirmation
9.4 ms
AUTH LATENCY
32
PROTOCOL STEPS
~2 s
RE-AUTH CYCLE

## Slide 6
EMERGENCY LOGIC
Two Independent Signals Must Both Be True
🔐 SIGNAL A — V2X Authentication Chain
"WHO is the emergency"
Ambulance OBU generates AuthRequest
→ RSU validates (ECDSA + timestamp)
→ ECDH session keys derived
→ Post-auth: is_emergency: true
→ RSU broadcasts EMERGENCY_ACTIVE
→ UDP to 192.168.0.255:5001
→ Car receives, sets _emergency = True
📡 SIGNAL B — Direct Position Sharing
"WHERE is the ambulance — no laptop needed"
Ambulance reads AprilTag zone
→ JSON: {role: ambulance, zone: 7}
→ UDP broadcast 192.168.0.255:5002
→ 10 Hz — purely Pi-to-Pi WiFi
→ Car stores amb_zone = 7
→ Freshness check: < 3 s old
→ _position_known() = True
YIELD DECISION:
No V2X signal
→ Follow lane normally
V2X active, no position
→ Wait for position fix
Both active + amb ≤ 3 zones behind
→ YIELD TRIGGERED

## Slide 7
EMERGENCY RESPONSE
5-State Yield Sequence
NORMAL
→
EVADING
→
HOLDING
→
RECOVERING
→
RESUMING
EVADING
Turns right toward inner island (yellow line). Proportional yellow-repel steering. Exits when yellow line detected or 2 s timer fires.
HOLDING
Creeps slowly along inner island wall. Exits when: ambulance passes (amb_zone > own_zone) + 1 s grace period OR V2X clears OR 30 s timeout.
RECOVERING
Arcs left back toward white line. Gyro mode: exits at 30° of measured yaw rotation. Timer fallback if IMU data is noisy.
RESUMING
Ramps speed 0 → normal over 2 s. Smooth re-entry to full-speed lane following. No jerk — gradual velocity ramp.
Key: while HOLDING the car uses its frozen last-known zone + the ambulance's live UDP zone stream to detect when the ambulance has passed — no inner tags needed.

## Slide 8
COMPUTER VISION
Real-Time Lane Following at 20 Hz
①
Grab 320×240 frame
Camera faces DOWN at the track surface
②
Crop top 40%
Remove far-field perspective distortion
③
HSV threshold — white line
Find centroid X of largest white contour
④
Proportional steering
wz = −kP × (centroid_x − centre) / (width/2)
⑤
Yellow repulsion
Override steering if yellow boundary too close
⑥
Detect AprilTag (every 3rd frame)
Update zone → broadcast to peer via UDP
LIVE VISION STREAM http://robot-ip:5005/
─────────────────────────────────────────
V2X_CAR_01 23:14:05
[Full camera frame 640px wide]
─── crop boundary ───────────────────
[LANE overlay] │ [HSV MASK]
green=centre │ grey = white px
red=centroid │ yellow= yellow px
──────────────────────────────────────
CAR z=3 AMB z=7 vx=0.20 NORMAL
ARMED AUTO V2X:ACTIVE PI:52.3°C
3 SWAPPABLE ALGORITHMS
centroid
Production default
pure pursuit
Geometric path
recorded path
Replay motor commands
Failure modes are always safe: no white >4s → slow · no white >8s → stop · no position → wait · V2X drops → stop yielding

## Slide 9
HUMAN-MACHINE INTERFACE
Real-Time WebSocket Dashboard
V2X AUTHENTICATION DASHBOARD
─────────────────────────────────────────────
ENTITIES: 3 (RSU · V2X · V2X_EMGY)
● RSU ONLINE — No
● V2X ONLINE — No
● V2X_EMGY ONLINE 🚑 Yes
EMERGENCY PRIORITY GRANTS: 147
SESSION_ESTABLISHED: 12
POST_AUTH_HMAC_FAIL: 0
FAILURES: 0
AVG AUTH LATENCY: 9.4 ms
WHAT THE DASHBOARD SHOWS
• All entities online/offline with heartbeat watchdog
• Emergency flag per entity — live via WebSocket
• Session event counts — no page refresh needed
• Authentication latency — rolling average
• POST_AUTH_HMAC_FAIL — instant failure visibility
• Entity marks OFFLINE within ~50 s of crash
• SQLite audit log — full event history on disk
WebSocket
LIVE PUSH, NO REFRESH
10 Hz
POSITION UPDATES
SQLite
AUDIT LOG
MJPEG
VISION STREAM :5005
50 s
OFFLINE WATCHDOG

## Slide 10
FUTURE-PROOFING
Post-Quantum Cryptography — Interface Ready
Classical ECDSA and ECDH are breakable by Shor's algorithm on a quantum computer. This platform abstracts all cryptography behind a single interface — switching to post-quantum requires changing one line in a config file. The 32-step protocol does not change.
// crypto_provider.h — pure virtual interface
virtual encapsulate();
virtual decapsulate();
virtual sign();
virtual verify();
virtual derive_keys();
// rsu_config.json — one line to switch:
"crypto_provider": "lattice" // was: "placeholder"
PLANNED ALGORITHMS
CRYSTALS-Dilithium
Replaces ECDSA signatures (NIST FIPS 204)
CRYSTALS-Kyber
Replaces ECDH key encapsulation (NIST FIPS 203)
LWE-based hardness
Resistant to Shor's algorithm on quantum computers
ALL SWAPPABLE LAYERS
Lane algorithm
centroid / pure pursuit / recorded-path — one line in config.yaml
Motor controller
Lyra protocol over UART — retarget firmware without touching Python
AprilTag layout
n_inner_tags / n_outer_tags — yield logic adapts automatically
Crypto provider
placeholder (ECDH) → lattice (Kyber) — one JSON key
Robot scale
Multiple cars + multiple ambulances — all work simultaneously

## Slide 11
SCOPE
Ten Engineering Domains. One System.
Embedded Systems
STM32F405, RTOS, hardware encoders × 4, custom-designed PCB
Computer Vision
Real-time lane detection + AprilTag localisation under real lighting
Robotics
5-state emergency evasion, closed-loop velocity, 3 swappable algorithms
V2X Networking
OBU/RSU architecture, 32-step mutual auth, UDP broadcast
Applied Cryptography
ECDH, ECDSA, HKDF, AES-256-GCM, HMAC-SHA-256, PQ interface
Distributed Systems
Multi-node coordination — no central controller, peer failure tolerant
Real-Time Control
20 Hz RTOS motor loop, never preempted
HMI
WebSocket dashboard, MJPEG video stream with live telemetry overlay
Edge Computing
Full stack on Raspberry Pi 5 — no cloud at runtime
Autonomous Navigation
Centroid, pure pursuit, recorded-path — tunable per deployment
This platform contains enough material for four independent final-year projects. This work required all four to exist simultaneously and operate as a single system.

## Slide 12
STATUS
What's Live. What's Next.
OPERATIONAL NOW
V2X Auth — 32-step mutual protocol
Live
Robot mobility — lane following
Live
Emergency evasion — 5-state machine
Live
Real-time WebSocket dashboard
Live
Gyro-based RECOVERING exit
Live
Dead-reckoning position (encoders)
Live
End-to-end auth latency
9.4 ms
Post-quantum — LatticeProvider
Interface ready
FOUR TARGETED IMPROVEMENTS
1
Geometry-based RECOVERING
Integrate gyro_z from STM32 to measure actual degrees turned (30°) instead of waiting for a timer.
2
Dead-reckoning between tags
Continuous position from wheel encoder ticks; resets on every AprilTag sighting.
3
Variable crop ratio by state
NORMAL: 40% · EVADING: 20% · RECOVERING: 0% — wider view during manoeuvres.
4
Post-quantum — Kyber + Dilithium
Plug into existing LatticeProvider interface. Protocol unchanged.
No new hardware required for improvements 1–3. STM32 already sends gyro_z and wheel_ticks[4].

## Slide 13
In one sentence
This project demonstrates authenticated V2X emergency vehicle priority — from cryptographic session establishment to physical lane evasion — on autonomous vehicles operating in the real world, on real hardware, with no simulation and no human intervention at any stage.
The cryptography is invisible to someone standing at the side of the table. What is visible is: the car moves, the ambulance passes, the car resumes. Nobody is thinking about the mathematics. They are thinking: this works.
Siliris Technologies Pvt. Ltd. · 2026